## Slide 1: Flash-Cosmos In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory Jisung Park, Roknoddin Azizi, Geraldo F. Oliveira, Mohammad Sadrosadati, Rakesh Nadig, David Novo, Juan Gómez Luna, Myungsuk Kim, and Onur Mutlu Published at MICRO 2022
Rakesh Nadig
P&S PIM
31 January 2023

## Slide 2: Executive Summary
Background: Bulk bitwise operations are widely used in many important data-intensive applications, e.g., databases, graph processing, cryptography etc.
Problem:
  Performance and energy efficiency of bulk bitwise operations are bottlenecked by 1) data movement between storage and the compute unit in traditional systems and in-storage processing (ISP) 2) data sensing (serial reading of operands) in prior in-flash processing (IFP) techniques
  Prior IFP techniques provide low reliability during computation
Goal: Improve performance, energy efficiency and reliability of bulk bitwise operations in in-flash processing
Key Ideas: Flash-Cosmos (Flash-Computation with One-Shot Multi-Operand Sensing) is an in-flash processing technique that is based on two key ideas:
  Multi-Wordline Sensing (MWS): Enables multi-operand bulk bitwise operations with a single sensing (read) operation
  Enhanced SLC-mode Programming (ESP): Increases the voltage margin between the erased and programmed states to provide higher reliability during in-flash computation
Key Results: Flash-Cosmos is evaluated using 160 real 3D NAND flash chips and with a state-of-the-art SSD simulator on three real-world workloads
  Flash-Cosmos improves the performance and energy efficiency by 3.5x and 3.3x over state-of-the-art IFP technique while providing high reliability during computation
1

## Slide 3: Talk Outline
Motivation
Background
Flash-Cosmos
Evaluation
Summary

## Slide 4: Bulk Bitwise Operations
Bulk Bitwise Operations
Web Search
Cryptography
Set Operations
Genome Analysis
Databases
Graph Processing
Hyper-dimensional
Computing
...
2

## Slide 5: Bulk Bitwise Operations
Bulk Bitwise Operations
Web Search
Cryptography
Set Operations
Genome Analysis
Databases
(database queries and indexing)
Graph Processing
Hyper-dimensional
Computing
...
Data movement between compute units and the memory hierarchy significantly affects the performance of bulk bitwise operations
2

## Slide 6: Data-Movement Bottleneck
Conventional systems perform outside-storage processing (OSP) after moving the data to host CPU through the memory hierarchy
Host Processor
(CPU, GPU)
Main
Memory
Write
Read
Storage
Write
Read
Memory Bandwidth tens to hundreds of GB/s
Storage I/O Bandwidth ~ 8 GB/s
Data Movement Bottleneck
External I/O bandwidth of storage systems is the main bottleneck for data movement in OSP
Computation
3

## Slide 7: NDP for Bulk Bitwise Operations
Near-Data
Processing
Cache
(e.g., Compute Cache1)
DRAM-based
main memory
(e.g., Ambit2)
In-Storage
(e.g., Biscuit4)
NVM-based
main memory
(e.g., Pinatubo3)
[1] Aga+, “Compute Caches," HPCA, 2017
[2] Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO, 2017
[3] Li+, “Pinatubo: A Processing-in-Memory Architecture for Bulk Bitwise Operations in Emerging Non-Volatile Memories,” DAC, 2016
[4] Gu+, “Biscuit: A Framework for Near-Data Processing of Big Data Workloads,” ISCA, 2016
[5] Gao+, “ParaBit: Processing Parallel Bitwise Operations in NAND Flash Memory Based SSDs,” MICRO, 2021
In-Flash
(e.g., ParaBit5)
...
Our focus
Large data sets
that do not fit
in main memory
4

## Slide 8: In-Storage Processing (ISP)
ISP performs computation using an in-storage computation unit (embedded cores or FPGA)
ISP reduces external data movement by transferring only the computation results to the host
Host Processor
(CPU, GPU)
Main
Memory
Result
Memory Bandwidth tens to hundreds of GB/s
Storage External I/O Bandwidth ~ 8 GB/s
In-Storage Computation Unit
⋯
NAND
Chip #1
NAND
Chip #4
⋯
NAND
Chip #1
NAND
Chip #4
⋯
Storage
Read
Result
Storage Internal I/O Bandwidth ~ 9.6 GB/s
Data Movement Bottleneck
Computation
5

## Slide 9: In-Storage Processing (ISP)
ISP performs computation using the in-storage computation unit
ISP reduces external data movement by transferring only the computation results to the host
Processor
(CPU, GPU)
Main
Memory
Read
Memory Bandwidth tens to hundreds of GB/s
Storage External I/O Bandwidth ~ 8 GB/s
In-Storage Computation Unit
⋯
NAND
Chip #1
NAND
Chip #4
⋯
NAND
Chip #1
NAND
Chip #4
⋯
Storage
Read
Read
Storage Internal I/O Bandwidth ~ 9.6 GB/s
Data Movement Bottleneck
Storage internal I/O bandwidth is the main bottleneck in ISP
5

## Slide 10: In-Flash Processing (IFP)
IFP performs computation within the flash chips as the data operands are being read serially
IFP reduces the internal data movement bottleneck in storage by transferring only the computation results to the in-storage computation unit
Host Processor
(CPU, GPU)
Main
Memory
Result
Memory Bandwidth tens to hundreds of GB/s
Storage External I/O Bandwidth ~ 8 GB/s
In-Storage Computation Unit
⋯
NAND
Chip #1
NAND
Chip #4
⋯
NAND
Chip #1
NAND
Chip #4
⋯
Storage
Result
Result
Storage Internal I/O Bandwidth ~ 9.6 GB/s
Data Sensing Bottleneck
Computation
6

## Slide 11: Data Sensing Bottleneck in IFP
In-Storage Computation Unit
⋯
NAND
Chip #1
NAND
Chip #4
⋯
NAND
Chip #1
NAND
Chip #4
⋯
State-of-the-art IFP technique [1] performs bulk bitwise operations by controlling the latching circuit of the page buffer
A
NAND Flash Chip
Page Buffer
Operand A
Operand B
Operand C
Operand D
…
[1] Gao+, “ParaBit: Processing Parallel Bitwise Operations in NAND Flash Memory Based SSDs,” MICRO, 2021
7

## Slide 12: Data Sensing Bottleneck in IFP
State-of-the-art IFP technique performs bulk bitwise operations by controlling the latching circuit of the page buffer
A
NAND Flash Chip
A
B
…
C
D
Page Buffer
Data Sensing
A
A
7

## Slide 13: Data Sensing Bottleneck in IFP
State-of-the-art IFP technique performs bulk bitwise operations by controlling the latching circuit of the page buffer
A
NAND Flash Chip
A
B
…
C
D
Page Buffer
A
B
Data Sensing
A AND B
7

## Slide 14: Data Sensing Bottleneck in IFP
State-of-the-art IFP technique performs bulk bitwise operations by controlling the latching circuit of the page buffer
NAND Flash Chip
A
B
…
C
D
Page Buffer
A AND B
Data Sensing
C
A AND B AND C
7

## Slide 15: Data Sensing Bottleneck in IFP
State-of-the-art IFP technique performs bulk bitwise operations by controlling the latching circuit of the page buffer
NAND Flash Chip
A
B
…
C
D
Page Buffer
A AND B
Data Sensing
C
A AND B AND C
Serial data sensing is the bottleneck in in-flash processing techniques
7

## Slide 16: Reliability Issues in IFP
NAND Flash memory suffers from high raw-bit error rate due to many sources of disturbances
ECC and data-randomization techniques are used to improve the reliability of flash memory
Prior IFP approaches cannot leverage ECC and data-randomization techniques as computation is performed within the flash chips during data sensing
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE, 2017
8

## Slide 17: Reliability Issues in IFP
Prior IFP approaches suffer from erroneous computation results due to high raw-bit error rate of NAND flash memory
A
NAND Flash Chip
A
B
…
C
D
Page Buffer
8

## Slide 18: Reliability Issues in IFP
Prior IFP approaches suffer from erroneous computation results due to high raw-bit error rate of NAND flash memory
NAND Flash Chip
B
…
C
D
Page Buffer
A
Data Sensing
B
A
8

## Slide 19: Reliability Issues in IFP
Prior IFP approaches suffer from erroneous computation results due to high raw-bit error rate of NAND flash memory
NAND Flash Chip
B
…
C
D
Page Buffer
A
A
Data Sensing
B
B
A AND B
8

## Slide 20: Reliability Issues in IFP
Prior IFP approaches suffer from erroneous computation results due to high raw-bit error rate of NAND flash memory
NAND Flash Chip
B
…
C
D
Page Buffer
A
A
Data Sensing
B
B
A AND B
Prior IFP techniques require the application to be highly error-tolerant
8

## Slide 21: Our Goal
Address the bottleneck of state-of-the-art IFP techniques
(serial sensing of operands)
Make IFP reliable
(provide accurate computation results)
9

## Slide 22: Our Proposal
Flash-Cosmos
  Enables Computation on multiple operands using a single sensing operation
  Provides high reliability during in-flash computation
NAND Flash Chip
B
…
D
Page Buffer
C
A
Simultaneous data Sensing
B
A
C
A AND B AND C
10

## Slide 23: Talk Outline
Motivation
Background
Flash-Cosmos
Evaluation
Summary

## Slide 24: NAND Flash Basics: A Flash Cell
A flash cell stores data by adjusting the amount of charge in the cell
Erased Cell
(Low Charge Level)
1
Programmed Cell
(High Charge Level)
0
Activation
Operates as a resistor
Operates as an open switch
11

## Slide 25: NAND Flash Basics: A NAND String
A set of flash cells are serially connected to form a NAND String
1
0
0
1
0
Bitline (BL)
…
NAND String
12

## Slide 26: NAND Flash Basics: Read Mechanism
NAND flash memory reads data by checking the bitline current
1
0
0
1
0
Bitline (BL)
Non-Target Cells:
Operate as resistors regardless of stored data
…
NAND String
13

## Slide 27: NAND Flash Basics: Read Mechanism
NAND flash memory reads data by checking the bitline current
1
0
0
1
0
Bitline (BL)
Non-Target Cells:
Operate as resistors regardless of stored data
…
NAND String
Target Cells:
Operate as resistors (1) or open switches (0)
13

## Slide 28: NAND Flash Basics: Read Mechanism
NAND flash memory reads data by checking the bitline current
1
0
0
1
0
BLi
Non-Target Cells:
Operate as resistors regardless of stored data
…
NAND String
Target Cells:
Operate as resistors (1) or open switches (0)
0
1
1
0
1
BLj
…
Reads as ‘1’
if BL current
flows
Reads as ‘0’
if BL current
cannot flow
13

## Slide 29: NAND Flash Basics: A NAND Flash Block
NAND strings connected to different bitlines comprise a NAND block
BL1
BL2
BL3
BL4
BL5
1
0
0
1
0
BLN
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
…
…
…
…
…
WL1
WL2
WL3
WL4
WLM
Block
A single wordline (WL) controls a large number of flash cells: High bit-level parallelism
14

## Slide 30: NAND Flash Basics: Block Organization
A large number of blocks share the same bitlines
BL1
BL2
BL3
BL4
BL5
BLN
…
…
…
…
Block2
…
…
…
…
…
…
…
…
…
BlockK
…
…
…
…
…
…
…
…
…
Block1
…
…
…
…
…
…
…
…
…
…
…
15

## Slide 31: Similarity to Digital Logic Gates
A large number of blocks share the same bitlines
BL1
BL2
BL3
BL4
BL5
BLN
…
…
…
…
Block2
…
…
…
…
…
…
…
…
…
BlockK
…
…
…
…
…
…
…
…
…
Block1
…
…
…
…
…
…
…
…
…
…
…
Cells in the same block are connected serially: Similar to digital AND
A
B
A•B
2-input AND
16
Notes: Our key observation is that NAND flash memory has similar organization to digital AND logic, as multiple cells are serially connected to the bitline, [Click] and

## Slide 32: Similarity to Digital Logic Gates
A large number of blocks share the same bitlines.
BL1
BL2
BL3
BL4
BL5
BLN
…
…
…
…
Block2
…
…
…
…
…
…
…
…
…
BlockK
…
…
…
…
…
…
…
…
…
Block1
…
…
…
…
…
…
…
…
…
…
…
Cells in the same block are connected serially: Similar to digital AND
A
B
A•B
2-input AND
Cells in different blocks
are connected in parallel: Similar to digital OR
2-input OR
A
B
A+B
16
Notes: It also similar to digital OR logic, in that multiple NAND strings are connected to the bitline in parallel. [Click]

## Slide 33: Talk Outline
Motivation
Background
Flash-Cosmos
Evaluation
Summary

## Slide 34: Flash-Cosmos: Overview
Enables in-flash bulk bitwise operations on multiple operands with a single sensing operation using Multi-Wordline Sensing (MWS)
17

## Slide 35: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block
  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Blocki
18

## Slide 36: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block
  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Blocki
Non-Target Cells:
Operate
as resistors

## Slide 37: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block
  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Non-Target Cells:
Operate
as resistors
Target Cells:
Operate
as resistors (1) or open switches (0)
0
0
0
1
Result:
18

## Slide 38: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block
  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Non-Target Cell:
Operate
as a resistance
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
1
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells
18

## Slide 39: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block
  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
0
Result:
18

## Slide 40: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block
  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
0
Result:
A bitline reads as ‘0’ even if one target cell stores ‘0’
 Equivalent to the bitwise AND of all the target cells
18

## Slide 41: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block
  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
1
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
1
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells
Flash-Cosmos (Intra-Block MWS) enables
bitwise AND of multiple pages in the same block
via a single sensing operation
18

## Slide 42: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks
  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
1
1
0
0
…
WLy in Blocki
…
…
…
…
19

## Slide 43: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks
  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
0
Result:
19

## Slide 44: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks
  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
0
Result:
A bitline reads as ‘0’ only when all the target cells store ‘0’
 Equivalent to the bitwise OR of all the target cells
19

## Slide 45: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks
  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLz in Blockj
19
Notes: Like intra-block MWS, [Click] this property holds when we activate more than two wordlines in different blocks at the same time, [Click], as we can see …

## Slide 46: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks
  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLz in Blockj
A bitline reads as ‘1’ only when one of the target cells store ‘1’
 Equivalent to the bitwise OR of all the target cells
19

## Slide 47: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks
  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLz in Blockj
Flash-Cosmos (Inter-Block MWS) enables
bitwise OR of multiple pages in different blocks
via a single sensing operation
19

## Slide 48: Supporting Other Bitwise Operations
Exploit Inverse Read[1] which is supported in modern NAND flash memory for copy-back operations
Bitwise NOT
Use Inverse Read operation with bitwise AND/OR operation
Bitwise NAND/ NOR
Use XOR between the latches[2] which is also supported in NAND flash memory
Bitwise XOR/XNOR
[1] Lee+, “High-Performance 1-Gb-NAND Flash Memory with 0.12-µm Technology,” JSSC, 2002
[2] Kim+, “A 512-Gb 3-b/Cell 64-Stacked WL 3-D-NAND Flash Memory,” JSSC, 2018
20

## Slide 49: Flash-Cosmos: Overview
Increases the reliability of in-flash bulk bitwise operations by using Enhanced SLC-mode Programming (ESP)
Enables in-flash bulk bitwise operations on multiple operands with a single sensing operation using Multi-Wordline Sensing (MWS)
21

## Slide 50: Enhanced SLC-Mode Programming (ESP)
SLC-mode programming provides a large voltage margin between the erased and programmed states
SLC-mode programming is still highly error-prone without the use of ECC and data-randomization
# of cells
Erased
0
Prog.
1
Threshold voltage
Voltage margin in SLC-mode
22

## Slide 51: Enhanced SLC-Mode Programming (ESP)
ESP further increases the voltage margin between the erased and programmed states
A wider voltage margin between the two states improves reliability by making the cells less vulnerable to errors
Perform additional steps in the incremental step pulse programming (ISPP) scheme to increase the voltage margin
0
Prog.
ESP
Increased voltage margin in ESP
# of cells
Erased
0
Prog.
1
Threshold voltage
22

## Slide 52: Enhanced SLC-Mode Programming (ESP)
ESP increases the voltage margin between the erased and programmed states
A wider voltage margin between the two states improves reliability during data sensing by making the cells less vulnerable to errors
0
Prog.
ESP
Increased voltage margin in ESP
# of cells
Erased
0
Prog.
1
Threshold voltage
ESP improves the reliability of in-flash computation without the use of ECC or data-randomization techniques
22

## Slide 53: Enhanced SLC-Mode Programming (ESP)
ESP increases the voltage margin between the erased and programmed states
A wider voltage margin between the two states improves reliability during data sensing by making the cells less vulnerable to errors
0
Prog.
ESP
Increased voltage margin in ESP
# of cells
Erased
0
Prog.
1
Threshold voltage
ESP can improve the reliability of prior in-flash processing techniques as well
22

## Slide 54: New Flash Commands
Three new commands to support Flash-Cosmos
MWS command to be used for,
  Intra- and inter-block MWS
  Inverse read
  Accumulation of results of all reads
ISCM command slot allows the flash controller to turn on/off four features,
  Inverse-read mode (I)
  Sensing-latch (S-latch) initialization (S)
  Cache-latch (C-latch) initialization (C)
  Move data from S-latch to C-latch (M)
Inverse read/S-latch init./C-latch init./Move
Block Addr.
Page Bitmap
MWS
ISCM
ADDR
CONT
CONF
ADDR
×3
BLK1
BLK2
PBM1
…
PBMN
(a)
ESP
ADDR
DATA
CONF
BLK1
BLK2
WL1
WL2
(b)
(c)
XOR
CONF
23

## Slide 55: New NAND Commands
Three new commands to support Flash-Cosmos
Page Bitmap (PBM) to specify the WLs to be activated for MWS operations
Four address slots for inter-block MWS command
ESP command works like a regular program command
XOR command performs bitwise XOR between the sensing and cache latches and stores the result in C-latch
Inverse read/S-latch init./C-latch init./Move
Block Addr.
Page Bitmap
MWS
ISCM
ADDR
CONT
CONF
ADDR
×3
BLK1
BLK2
PBM1
…
PBMN
(a)
ESP
ADDR
DATA
CONF
BLK1
BLK2
WL1
WL2
(b)
(c)
XOR
CONF
23

## Slide 56: Operational Example
ISCM
BLK
PBM
BLK
PBM
1
2
3
4
A
Flash-Cosmos
NAND Flash Chip
Plane#2
Plane#1
A
B
C
D
16KiB
1
2
3
4
D
1
2
3
4
1
2
3
4
B
C
MWS
1111
CONT
CONF
0011
0101
0100
1010
MWS
0001
CONT
CONF
0001
0001
0010
1111
Blk1
Blk2
Blk3
Blk4
Blk: 3
WLs: 1&3
Blk: 4
WLs: 2&4
(C1 • C3)
+(D2 • D4)
(C1+C3) •(D2+D4)≡
❶
A1+(B1 • B2 • B3 • B4)
❷
Blk: 1
WLs: 1
Blk: 2
WLs: all
{A1+(B1 • B2 • B3 • B4)} •(C1+C3) •(D2+D4)
24

## Slide 57: Operational Example
ISCM
BLK
PBM
BLK
PBM
1
2
3
4
A
Flash-Cosmos
NAND Flash Chip
Plane#2
Plane#1
A
B
C
D
16KiB
1
2
3
4
D
1
2
3
4
1
2
3
4
B
C
MWS
1111
CONT
CONF
0011
0101
0100
1010
MWS
0001
CONT
CONF
0001
0001
0010
1111
Blk1
Blk2
Blk3
Blk4
Blk: 3
WLs: 1&3
Blk: 4
WLs: 2&4
(C1 • C3)
+(D2 • D4)
(C1+C3) •(D2+D4)≡
❶
A1+(B1 • B2 • B3 • B4)
❷
Blk: 1
WLs: 1
Blk: 2
WLs: all
{A1+(B1 • B2 • B3 • B4)} •(C1+C3) •(D2+D4)
Bit vectors Ci and Di are programmed with their inverse data for the bitwise OR operation
24

## Slide 58: Operational Example
ISCM
BLK
PBM
BLK
PBM
1
2
3
4
A
Flash-Cosmos
NAND Flash Chip
Plane#2
Plane#1
A
B
C
D
16KiB
1
2
3
4
D
1
2
3
4
1
2
3
4
B
C
MWS
1111
CONT
CONF
0011
0101
0100
1010
MWS
0001
CONT
CONF
0001
0001
0010
1111
Blk1
Blk2
Blk3
Blk4
Blk: 3
WLs: 1&3
Blk: 4
WLs: 2&4
(C1 • C3)
+(D2 • D4)
(C1+C3) •(D2+D4)≡
❶
A1+(B1 • B2 • B3 • B4)
❷
Blk: 1
WLs: 1
Blk: 2
WLs: all
{A1+(B1 • B2 • B3 • B4)} •(C1+C3) •(D2+D4)
  Issue an MWS command for (C1+C3)•(D2+D4) by enabling inverse-read mode and initialization of sensing and cache latches
24

## Slide 59: Operational Example
ISCM
BLK
PBM
BLK
PBM
1
2
3
4
A
Flash-Cosmos
NAND Flash Chip
Plane#2
Plane#1
A
B
C
D
16KiB
1
2
3
4
D
1
2
3
4
1
2
3
4
B
C
MWS
1111
CONT
CONF
0011
0101
0100
1010
MWS
0001
CONT
CONF
0001
0001
0010
1111
Blk1
Blk2
Blk3
Blk4
Blk: 3
WLs: 1&3
Blk: 4
WLs: 2&4
(C1 • C3)
+(D2 • D4)
(C1+C3) •(D2+D4)≡
❶
A1+(B1 • B2 • B3 • B4)
❷
Blk: 1
WLs: 1
Blk: 2
WLs: all
{A1+(B1 • B2 • B3 • B4)} •(C1+C3) •(D2+D4)
Issue an MWS command for {A1+(B1 • B2 • B3 • B4)} while disabling the inverse-read mode and initialization of both latches
24

## Slide 60: Operational Example
ISCM
BLK
PBM
BLK
PBM
1
2
3
4
A
Flash-Cosmos
NAND Flash Chip
Plane#2
Plane#1
A
B
C
D
16KiB
1
2
3
4
D
1
2
3
4
1
2
3
4
B
C
MWS
1111
CONT
CONF
0011
0101
0100
1010
MWS
0001
CONT
CONF
0001
0001
0010
1111
Blk1
Blk2
Blk3
Blk4
Blk: 3
WLs: 1&3
Blk: 4
WLs: 2&4
(C1 • C3)
+(D2 • D4)
(C1+C3) •(D2+D4)≡
❶
A1+(B1 • B2 • B3 • B4)
❷
Blk: 1
WLs: 1
Blk: 2
WLs: all
{A1+(B1 • B2 • B3 • B4)} •(C1+C3) •(D2+D4)
By disabling the initialization of latches, the result of the two MWS commands are accumulated in sensing and cache latches
24

## Slide 61: Talk Outline
Motivation
Background
Flash-Cosmos
Evaluation
Summary

## Slide 62: Evaluation Methodology
We evaluate Flash-Cosmos using
160 real state-of-the-art 3D NAND flash chips
25

## Slide 63: Real Device Characterization
We validate the feasibility, performance, and reliability of Flash-Cosmos
160 48-layer 3D TLC NAND flash chips
  3,686,400 tested wordlines
Under worst-case operating conditions
  1-year retention time at 10K P/E cycles
  Worst-case data patterns
26

## Slide 64: Results: Real-Device Characterization
Both intra- and inter-block MWS operations
require no changes to the cell array
of commodity NAND flash chips
Both MWS operations can activate multiple WLs
(intra: up to 48, inter: up to 4) at the same time
with small increase in sensing latency (< 10%)
ESP significantly improves
the reliability of computation results
(zero bit error in the tested flash cells)
26
Notes: Through our real-device characterization, we demnostrated that both MWS operations are possible without requiring any change ot the cell array of commodity NAND flash chips, [Click] and they can reliably activate multiple wordlines at the same time without significant increase in sensing latency. [Click]
We also observed no errors in the tested cells when we program data using ESP, which shows that Flash-Cosmos enables reliable in-flash bulk bitwise operations. [Click]

## Slide 65: Evaluation Methodology
We evaluate Flash-Cosmos using
160 real state-of-the-art 3D NAND flash chips
Three real-world applications that perform bulk bitwise operations
27

## Slide 66: Evaluation With Real-World Workloads
Simulation
  MQSim [Tavakkol+, FAST’18] to model the performance of Flash-Cosmos and the baselines
Workloads
  Three real-world applications that heavily rely on bulk bitwise operations
  Bitmap Indices (BMI): Bitwise AND of up to ~1,000 operands
  Image Segmentation (IMS): Bitwise AND of 3 operands
  k-clique star listing (KCS): Bitwise OR of up to 32 operands
Baselines
  Outside-Storage Processing (OSP): a multi-core CPU (Intel i7 11700K)
  In-Storage Processing (ISP): an in-storage hardware accelerator
  ParaBit [Gao+, MICRO’21]: the state-of-the-art in-flash processing (IFP) mechanism
28

## Slide 67: Results: Performance & Energy
Speedup over OSP
Chart: 
| BMI | IMS | KCS | AVG
 | 1.3181 | 1.1935 | 1.3007 | 1.2794
 | 14.1649 | 2.9997 | 12.8867 | 9.2742
 | 198.4035 | 2.9998 | 25.8962 | 32.4204
ISP
ParaBit
Flash-Cosmos
Flash-Cosmos provides significant performance & energy benefits over all the baselines
Performance and energy benefits only increase with more number of operands
Chart: 
| BMI | IMS | KCS | AVG
ISP | 8.2558 | 5.4514 | 7.4777 | 7.1709
ParaBit | 49.449 | 8.7761 | 38.1762 | 29.1277
Flash-Cosmos | 582.8533 | 8.9811 | 76.5954 | 95.9386
Energy benefit over OSP
150×
14×
2.5×
20×
2×
70×
12×
1.6×
10×
2×
25×
3.5×
3.3×
13.4×
29
Notes: Add average

## Slide 68: More in the Paper
https://arxiv.org/abs/2209.05566.pdf
30
Notes: Direct to the PDF

## Slide 69: Talk Outline
Motivation
Background
Flash-Cosmos
Evaluation of Flash-Cosmos and Key Results
Summary

## Slide 70: Flash-Cosmos: Summary
First work to enable multi-operand bulk bitwise operations with a single sensing operation and high reliability
Improves performance by 3.5x/25x/32x on average over ParaBit/ISP/OSP
Improves energy efficiency by 3.3x/13.4x/95x on average over ParaBit/ISP/OSP
Low-cost & requires no changes to flash cell arrays
31

## Slide 71: Flash-Cosmos In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory Jisung Park, Roknoddin Azizi, Geraldo F. Oliveira, Mohammad Sadrosadati, Rakesh Nadig, David Novo, Juan Gómez Luna, Myungsuk Kim, and Onur Mutlu Published at MICRO 2022
Rakesh Nadig
P&S PIM
31 January 2023

## Slide 72: BACKUP SLIDES

## Slide 73: NAND Flash Programming
Avg. RBER [×10–3]
w/o data randomization
0
1
2
3
6
12
Retention age [months]
Avg. RBER [×10–3]
0
2
4
6
(a) SLC–mode programming
Chart: 
| 0 | 2 | 4 | 6 | 8 | 10
0K | 0.00086462 | 0.00098814 | 0.0011117 | 0.0013587 | 0.0016057 | 0.0018528
1K | 0.00098814 | 0.0011117 | 0.0012352 | 0.0014822 | 0.0017292 | 0.0019763
2K | 0.0011117 | 0.0012352 | 0.0014822 | 0.0017292 | 0.0019763 | 0.0023468
3K | 0.0012352 | 0.0014822 | 0.0017292 | 0.0019763 | 0.0023468 | 0.0027174
4K
5K
6K | 0.0017292 | 0.0019763 | 0.0022233 | 0.0024704 | 0.0028409 | 0.0032115
7K
8K
9K
10K | 0.0024704 | 0.0027174 | 0.0029644 | 0.003335 | 0.0037055 | 0.0040761
w/ data randomization
0
1
2
3
6
12
Retention age [months]
0
2
4
6
10K
6K
3K
2K
1K
0K
PEC:
Chart: 
 | 0.00012352 | 0.00037055 | 0.00049407 | 0.00061759 | 0.00074111 | 0.00086462
 | 0.00024704 | 0.00049407 | 0.00061759 | 0.00086462 | 0.00098814 | 0.0011117
 | 0.00037055 | 0.00061759 | 0.00074111 | 0.00098814 | 0.0011117 | 0.0013587
 | 0.00049407 | 0.00086462 | 0.0011117 | 0.0012352 | 0.0014822 | 0.0016057


 | 0.00086462 | 0.0012352 | 0.0014822 | 0.0017292 | 0.0019763 | 0.0022233



 | 0.0013587 | 0.0017292 | 0.0019763 | 0.0023468 | 0.0025939 | 0.0029644
(a) SLC–mode programming
# of cells
margin
V
TH
Prog.
1
V
TH
Retention
V
REF
loss
Interference
Erased
0
(b) MLC–mode programming
# of cells
E
11
V
TH
P1
01
P2
00
P3
10
MSB
V
REF1
LSB
V
REF2
V
REF3
margin
V
TH

## Slide 74: Outside-Storage Processing (OSP)
Moves every operand from the storage to the compute unit (CPU/GPU) for computation
Performs the computation and writes the results back to the SSD
External BW: 8 GB/s
Die#1
D#4
⋯
D#1
D#4
⋯
⋯
Channel#1
Channel#8
Channels
Internal BW:
9.6 (1.2×8) GB/s
SSD Controller
NAND Flash Array
Plane
Bit-Vectors
A
B
C
tR: 60 μs
tDMA: 27 μs
tEXT: 32 (4×8) μs
A:
B:
C:
OSP: Outside-Storage Processing
Bottleneck: External I/O

## Slide 75: Outside-Storage Processing (OSP)
Moves every operand from the storage to the compute unit (CPU/GPU) for computation
Performs the computation and writes the results back to the SSD
External BW: 8 GB/s
Die#1
D#4
⋯
D#1
D#4
⋯
⋯
Channel#1
Channel#8
Channels
Internal BW:
9.6 (1.2×8) GB/s
SSD Controller
NAND Flash Array
Plane
Bit-Vectors
A
B
C
tR: 60 μs
tDMA: 27 μs
tEXT: 32 (4×8) μs
A:
B:
C:
OSP: Outside-Storage Processing
Bottleneck: External I/O
Outside-Storage Processing is bottlenecked by data movement between the compute unit
and SSD (SSD external bandwidth)

## Slide 76: Outside-Storage Processing (OSP)
Moves every operand from the storage to the compute unit (CPU/GPU) for computation
Performs the computation and writes the results back to the SSD
External BW: 8 GB/s
Die#1
D#4
⋯
D#1
D#4
⋯
⋯
Channel#1
Channel#8
Channels
Internal BW:
9.6 (1.2×8) GB/s
SSD Controller
NAND Flash Array
Plane
Bit-Vectors
A
B
C
tR: 60 μs
tDMA: 27 μs
tEXT: 32 (4×8) μs
A:
B:
C:
OSP: Outside-Storage Processing
Bottleneck: External I/O
Near-Data Processing (NDP)
moves computation closer to where the data resides
is a promising approach to mitigate data movement

## Slide 77: In-Storage Processing (ISP)
Reads the operands from the NAND flash chips to the SSD Controller in a serial manner
Performs the computation in the SSD controller
Moves the computation result to the host
External BW: 8 GB/s
Die#1
D#4
⋯
D#1
D#4
⋯
⋯
Channel#1
Channel#8
Channels
Internal BW:
9.6 (1.2×8) GB/s
SSD Controller
NAND Flash Array
Plane
Bit-Vectors
A:
B:
C:
A
B
C
ISP: In-Storage Processing
Start computation & result transfer to host
Bottleneck: Internal I/O

## Slide 78: In-Storage Processing (ISP)
Reads the operands from the NAND flash chips to the SSD Controller in a serial manner
Performs the computation in the SSD controller
Moves the computation result to the host
External BW: 8 GB/s
Die#1
D#4
⋯
D#1
D#4
⋯
⋯
Channel#1
Channel#8
Channels
Internal BW:
9.6 (1.2×8) GB/s
SSD Controller
NAND Flash Array
Plane
Bit-Vectors
A:
B:
C:
A
B
C
ISP: In-Storage Processing
Start computation & result transfer to host
Bottleneck: Internal I/O
In-Storage Processing is bottlenecked by data movement between NAND flash memory and SSD controller (SSD internal bandwidth)

## Slide 79: In-Flash Processing (IFP)
Performs computation within the NAND flash chips
Moves only the computation results from the NAND flash chips to the SSD controller and host
External BW: 8 GB/s
Die#1
D#4
⋯
D#1
D#4
⋯
⋯
Channel#1
Channel#8
Channels
Internal BW:
9.6 (1.2×8) GB/s
SSD Controller
NAND Flash Array
Plane
Bit-Vectors
A:
B:
C:
A
B
C
IFP: In-Flash Processing
Bottleneck: Sensing
Start computation & result transfer to controller

## Slide 80: In-Flash Processing (IFP)
Performs computation within the NAND flash chips
Moves only the computation results from the NAND flash chips to the SSD controller and host
External BW: 8 GB/s
Die#1
D#4
⋯
D#1
D#4
⋯
⋯
Channel#1
Channel#8
Channels
Internal BW:
9.6 (1.2×8) GB/s
SSD Controller
NAND Flash Array
Plane
Bit-Vectors
A:
B:
C:
A
B
C
IFP: In-Flash Processing
Bottleneck: Sensing
Start computation & result transfer to controller
In-Flash Processing significantly reduces
data movement compared to OSP and ISP

## Slide 81: In-Flash Processing (IFP)
Performs computation within the NAND flash chips
Moves only the computation results from the NAND flash chips to the SSD controller and host
External BW: 8 GB/s
Die#1
D#4
⋯
D#1
D#4
⋯
⋯
Channel#1
Channel#8
Channels
Internal BW:
9.6 (1.2×8) GB/s
SSD Controller
NAND Flash Array
Plane
Bit-Vectors
A:
B:
C:
A
B
C
IFP: In-Flash Processing
Bottleneck: Sensing
Start computation & result transfer to controller
In-Flash Processing is bottlenecked
by data sensing

## Slide 82: Overview of three computation approaches
ISP
IFP
External BW: 8 GB/s
tR: 60 μs
tDMA: 27 μs
tEXT: 4 μs × 8
Die#1
D#4
⋯
D#1
D#4
⋯
⋯
Channel#1
Channel#8
Channels
Internal BW:
9.6 (1.2×8) GB/s
SSD Controller
NAND Flash Array
Plane
Bit-Vectors
A:
B:
C:
SSD organization
Channel#1 timeline
A
B
C
OSP
# channels
In-Flash processing significantly reduces data movement
Notes: Todo: Motivate the need for IFP

## Slide 83: Background
NAND Flash Organization
NAND Flash Package
Die#0
Die#1
⋯
Peripheral
Plane#0
Blk#1
Blk#2
Plane#1
Blk#1
Blk#2
⋯
⋯
⋯
⋯
BL1
BL2
BLn
Sub-block
⋯
⋯
⋯
⋯
⋯
⋯
WL1
WL2
WLm
⋯
NAND Flash Block
NAND
String

## Slide 84: Background
NAND flash read mechanism consists of three steps: 1) Precharge 2) Evaluation 3) Discharge
P Precharge
⋯
V
PRE
Latch
OFF
⋯
V
PASS
Target WL
V
REF
C
SO
SO
BL
String
NAND
≤
V
TH
V
REF
a
>
V
TH
V
REF
b
M
PRE
D Discharge
❹
E Evaluation
⋯
V
PRE
Latch
ON
V
PASS
V
REF
⋯
⋯
V
PRE
Latch
OFF
0
0
⋯
BL
BL

## Slide 85: Background
Precharge
P Precharge
⋯
V
PRE
Latch
OFF
⋯
V
PASS
Target WL
V
REF
C
SO
SO
BL
String
NAND
≤
V
TH
V
REF
a
>
V
TH
V
REF
b
M
PRE
D Discharge
❹
E Evaluation
⋯
V
PRE
Latch
ON
V
PASS
V
REF
⋯
⋯
V
PRE
Latch
OFF
0
0
⋯
BL
BL
Enable precharge transistor MPRE to charge all target BLs and their sense-out capacitors (CSO) to VPRE

## Slide 86: Background
Evaluation
❹
E Evaluation
⋯
V
PRE
Latch
ON
V
PASS
V
REF
⋯
BL
D Discharge
P Precharge
⋯
V
PRE
Latch
OFF
⋯
V
PASS
Target WL
V
REF
C
SO
SO
BL
String
NAND
≤
V
TH
V
REF
a
>
V
TH
V
REF
b
M
PRE
⋯
V
PRE
Latch
OFF
0
0
⋯
BL
Target WL
≤
V
TH
V
REF

## Slide 87: Background
Disconnect the BLs from VPRE and enable the latching circuit
Evaluation
❹
E Evaluation
⋯
V
PRE
Latch
ON
V
PASS
V
REF
⋯
BL
D Discharge
P Precharge
⋯
V
PRE
Latch
OFF
⋯
V
PASS
Target WL
V
REF
C
SO
SO
BL
String
NAND
≤
V
TH
V
REF
a
>
V
TH
V
REF
b
M
PRE
⋯
V
PRE
Latch
OFF
0
0
⋯
BL
Target WL
≤
V
TH
V
REF

## Slide 88: Background
If VTH ≤ VREF , the charge in CSO quickly flows through the NAND string (Sensed as 1)
Evaluation
❹
E Evaluation
⋯
V
PRE
Latch
ON
V
PASS
V
REF
⋯
BL
D Discharge
P Precharge
⋯
V
PRE
Latch
OFF
⋯
V
PASS
Target WL
V
REF
C
SO
SO
BL
String
NAND
≤
V
TH
V
REF
a
>
V
TH
V
REF
b
M
PRE
⋯
V
PRE
Latch
OFF
0
0
⋯
BL
Target WL
≤
V
TH
V
REF

## Slide 89: Background
Evaluation
❹
E Evaluation
⋯
V
PRE
Latch
ON
V
PASS
V
REF
⋯
BL
D Discharge
P Precharge
⋯
V
PRE
Latch
OFF
⋯
V
PASS
Target WL
V
REF
C
SO
SO
BL
String
NAND
≤
V
TH
V
REF
a
>
V
TH
V
REF
b
M
PRE
⋯
V
PRE
Latch
OFF
0
0
⋯
BL
Target WL
>
V
TH
V
REF
If VTH > VREF , the target cell blocks the BL discharge current (Sensed as 0)

## Slide 90: Background
Bitlines are discharged to return the NAND string to its initial state for future operations
Discharge
D Discharge
⋯
V
PRE
Latch
OFF
0
0
⋯
BL
❹
E Evaluation
⋯
V
PRE
Latch
ON
V
PASS
V
REF
⋯
BL
P Precharge
⋯
V
PRE
Latch
OFF
⋯
V
PASS
Target WL
V
REF
C
SO
SO
BL
String
NAND
≤
V
TH
V
REF
a
>
V
TH
V
REF
b
M
PRE

## Slide 91: Background
Latching circuit during read operation
OUT
OUT
M1
M2
BL
SO
M
PRE
V
PRE
VOUT :
VOUT :
VSO :
VTH ≤ VREF
PRECHARGE
0
1
1
OUT
OUT
M1
M2
BL
SO
M
PRE
V
PRE
VOUT :
VOUT :
VSO :
VTH ≤ VREF
EVALUATION
0
1
0
During precharge, the flash chip charges the BL, making VSO = 1
Before evaluation, the chip initializes the latching circuit by activating only transistor M1
Evaluation step disables MPRE and M1 while enabling M2
Charge in CSO quickly flows through the NAND string making VSO = 0 and VOUT = 1
Notes: Put banners explaining the working

## Slide 92: Background
Latching circuit during read operation
OUT
OUT
M1
M2
BL
SO
M
PRE
V
PRE
VOUT :
VOUT :
VSO :
VTH > VREF
PRECHARGE
0
1
1
OUT
OUT
M1
M2
BL
SO
M
PRE
V
PRE
VOUT :
VOUT :
VSO :
VTH > VREF
EVALUATION
1
0
1
If VTH > VREF , CSO cannot discharge due to the target cell acting as an open switch, leading to VSO = 1 and VOUT = 0

## Slide 93: Background
During precharge, the flash chip charges the BL, making ISO = 1
Before evaluation, the chip initializes the latching circuit by activating only transistor M2
Evaluation step disables MPRE and M2 while enabling M1
Charge in CSO quickly flows through the NAND string making ISO = 0 and IOUT = 1
Latching circuit during inverse read operation
OUT
OUT
M1
M2
BL
SO
M
PRE
V
PRE
IOUT :
IOUT :
ISO :
VTH ≤ VREF
PRECHARGE
1
0
1
OUT
OUT
M1
M2
BL
SO
M
PRE
V
PRE
IOUT :
IOUT :
ISO :
VTH ≤ VREF
EVALUATION
1
0
0

## Slide 94: Background
Latching circuit during inverse read operation
OUT
OUT
M1
M2
BL
SO
M
PRE
V
PRE
IOUT :
IOUT :
ISO :
VTH > VREF
PRECHARGE
1
0
1
OUT
OUT
M1
M2
BL
SO
M
PRE
V
PRE
IOUT :
IOUT :
ISO :
VTH > VREF
EVALUATION
0
1
1
If VTH > VREF , CSO cannot discharge due to the target cell acting as an open switch, leading to ISO = 1 and IOUT = 0